## On 20130123
### North American Datum
#### Introduction
The North American Datum is the official datum[1] used for the primary geodetic network in North America. In the fields of cartography and land-use there are currently two North American Datums in use: NAD27[2] and NAD83[3]. Both are geodetic reference systems, but each is based on different measurements.
[1] Taken from http://en.wikipedia.org/wiki/North_American_Datum
[2] North American Datum 1927
[3] North American Datum 1983
#### History
Efforts to supplement the various national surveying systems began in the 19th century.
A unified geodetic system for the whole world became essential in the 1950s.
International space science and the beginning of astronautics.
- The lack of inter-continental geodetic information.
- The inability of the large geodetic systems, such as European Datum (ED50), North American Datum, and Tokyo Datum, to provide a worldwide geo-data basis.
- Need for global maps for navigation, aviation, and geography.
- Western Cold War preparedness necessitated a standardised, NATO-wide geospatial reference system, in accordance with the NATO Standardisation Agreement.

#### NAD 27
It is based on the elipsoid of Clarke of 1866. These data were taken manualy from different survey of the entire continent. Meade Ranch is the base station in Kansas.

Ellipsoid	Semimajor axis†	Semiminor axis†	Inverse flattening††
Clarke 1866	6,378,206.4 m	6,356,583.8 m	294.978698214

†By definition. ††Calculated.

These are the defining dimensions for NAD27, but Clarke actually defined his 1866 spheroid as a = 20,926,062 British feet, b = 20,855,121 British feet. The conversion to meters uses Clarke's 1865 inch-meter ratio of 39.370432. In a practical sense, the length of a foot or meter at the time could not be benchmarked to better than about 0.02 mm, so the meter equivalents used now can be considered exact to well beyond the uncertainties in the lengths and conversion values of the time.

#### Reference ellipsoid
In geodesy, a reference ellipsoid[4] is a mathematically-defined surface that approximates the geoid, the truer figure of the earth, or other planetary body. Because of their relative simplicity, reference ellipsoids are used as a preferred surface on which geodetic network computations are performed and point coordinates such as latitude, longitude, and elevation are defined.
[4] http://en.wikipedia.org/wiki/Reference_ellipsoid
#### NAD 83
Because Earth deviates significantly from a perfect ellipsoid, the ellipsoid that best approximates its shape varies region by region across the world. Clarke 1866, and North American Datum of 1927 with it, were surveyed to best suit North America as a whole. Likewise, historically most regions of the world used ellipsoids measured locally to best suit the vagaries of earth's shape in their respective locales. While ensuring the most accuracy locally, this practice makes integrating and disseminating information across regions troublesome.
As satellite geodesy and remote sensing technology reached high precision and were made available for civilian applications, it became feasible to acquire information referred to a single global ellipsoid. This is because satellites naturally deal with Earth as a monolithic body.
Therefore the GRS80[5] ellipsoid was developed for best approximating the earth as a whole, and it became the foundation for the North American Datum of 1983. Though generally GRS 80 and its close relative WGS 84[6] are not the best fit for any given region, a need for the closest fit largely evaporates when a global survey is combined with computers, databases, and software able to compensate for local conditions. The latest revision is WGS 84 (dating from 1984 and last revised in 2004), which was valid up to about 2010. Before the following were used: WGS 72, WGS 66, and WGS 60.
[5] Geodetic Reference System 1980 see http://en.wikipedia.org/wiki/GRS_80
[6] The World Geodetic System is a standard for use in cartography, geodesy, and navigation see http://en.wikipedia.org/wiki/World_Geodetic_System.